## Slide 1: Logbook-Holiday

## Slide 2: Thesis-2015
Innovation:
  Microelectrode array
  Larger amount of data. 1.more info. 2. hard to transmit
  Limitation on size and power of the local devices.
Measuring methods
  Extracellular recordings. √
  Intracellular recordings
Signal Characters
  Signal of interests->300~6kHz
  Local field potential(LPF)-signal from other units->60Hz-

## Slide 3
Algorithms- reviewed
  NEO
  MTEO
  ->Upgrade to adaptive algorithm with dynamic thresholding
    RMS measuring with sliding window->threshold inflation
    With nonoverlapping window
  Robust statistics theory-based adaptive thresholding
    TEO->Hanning window->
      u mean, sigma std. P- user defined probability. ‘A high value of ‘p’ will decrease this probability but it will also decrease the probability of detecting true spikes. ‘
    Con. High complexity
  Absolute value & stationary WT
    Low SNR->SWT, High SNR -> absolute value
    High computational cost

## Slide 4
Parallel Spike detection
  Procedure
    1st pathway: MTEO/NEO
    2nd pathway: SAM
    Adaptive RMS thresholding (‘signal during a spike is not considered’ )
    ‘The adaptive thresholding algorithm only considers threshold crossings as spikes if they have occurred more than 15 samples since the last spike’
    Combining unique spikes
  Two pathway emphasis different features-> which features?
    NEO larger differences
    SAM large values

## Slide 5
Series Spike Detection
  Procedure
    NEO/SAM->SAM/NEO->Adaptive Thresholding
  Very distinguishable spikes after two emphasises, but maybe some small spikes are suppressed to nearly zero.

## Slide 6
Data
Simulation 1
easy2
Hard2
Real-not sure

## Slide 7: Some ideas
New operator
  Two subtractions, one multiplication. Less computation than NEO
Difference between spike and noise
New methods
1.
Converge to a single elastic algorithm